GENERIC SPECIFICATION FOR Meter Enclosure

GE Multilin Meter Enclosure

1. PRODUCT

## 1.2	MANUFACTURER

## General Electric Company products have been used as the basis for design.  Other manufactures’ products of equivalent quality and operating features may be acceptable, at the engineer’s discretion, if they comply with all requirements specified or indicated in these Contract documents.

1.2 Meter Enclosure

- The meter enclosure shall be UL and cUL listed.

- The meter enclosure shall be NEMA1 rated.

- The meter enclosure shall have two options:  120V and 277V (with Control Power Transformer)

- The meter enclosure shall have a locking cabinet with a tagging and locking functionality

- The meter enclosure shall be delivered and tested from the manufacturer with the GE EPM2200/6000/6010/7000 meter installed.

- The meter enclosure shall have standard equipment including voltage fuses, a shorting block and a control power transformer for a 277V configuration.

- The meter enclosure shall be made out of steel and internally and externally ANSI 49 Grey.

- The meter enclosure shall have labels internally describing inputs.

- The meter enclosure shall have punch outs for feeding wires.

- The meter enclosure should match the following dimensions:

Height of Meter Enclosure including mounting holes:  13.50 inches

Width of Meter Enclosure including mounting holes:  10.27 inches

Width of Meter Enclosure including locking bracket:  11.06 inches

Depth of Meter Enclosure without meter:	7.28 inches

Depth of Meter Enclosure: with meter:	8.081 inches

Length between Mounting Holes:		12.75 inches

Width between Mounting Holes:		8.000 inches

- The acceptable product is General Electric Company, Multilin Meter Enclosure